|  | QC Flooring Item Description Unit Quantity Rate Total 1. The permanent formwork shall be QC Flooring 54/250, 54mm deep x 250mm wide with Z275 spelter Galvanised deep troughed interlocking Commercial Quality steel units/panels. Standard QC Flooring units/panels or QC Flooring Un-propped/Propless units/panels. Un-propped or Propless QC Panel dimension DEPTH / WIDTH varies. QC Units are available in a Plain or Embossed finish. Specify QC Flooring Units (Thickness)mm Galvanised Z275 spelter OR a Chromadek® paint finish on one side with a Pebble Grey backer on the reverse side. ISQ 300 1.0mm in a Galvanised Z275 spelter ISQ 300 1.0mm in a Galvanised Z275 spelter with a Chromadek® paint finish on one side and Pebble Grey backer on the reverse side ISQ 300 1.2mm in a Galvanised Z275 spelter ISQ 300 1.2mm in a Galvanised Z275 spelter with a Chromadek® paint finish on one side and Pebble Grey backer on the reverse side ISQ 300 1.6mm in a Galvanised Z275 spelter ISQ 300 2.0mm in a Galvanised Z275 spelter Note: Please contact the manufacturer for load tables and QC Unpropped/Propless dimensions and/or sizes to suit. Manufacturer: Global Roofing Solutions: Tel. 011 898-2900 M² 2. Kerb Flashing 25 x 50 x depth of the slab. Available in 0.8mm, 1.0mm and 1.2mm Z275 spelter Galvanised steel. Lm 3. Drip Kerb Flashing 25 x 25 x 35 x 50 x Depth of slab available in 0.8mm, 1.0mm, 1.2mm Z275 spelter Galvanised Steel. Lm 4. Galvanised Steel Strapping to secure flashing (1000mm) Lm 5. QC Clips, Girth ±100mm x Width 20mm (2mm Thick – Commercial Grade Steel) - Clips to be installed at ±500mm centres. No 6. Pop Rivets 4.8 x15mm long No 7. Hex Head Screws 14 x 25mm No 8. Hammer Drive Screws (Require 2x per QC unit at end of bearing points) No 8. Heavy Duty Vice Grip Tool (for crimping the QC Clips) No Note: For special requirements contact Global Roofing Solutions Tel. 011 898-2900 |  |
| --- | --- | --- |